## Slide 1: Computer Architecture
Prof. Saurabh Gandhi (EEE department)

## Slide 2: The computer we have built so far

## Slide 3: What happens if
A garbage instruction gets into the pipeline?
An instruction misbehaves (divide by zero, or arithmetic overflow)?
An interrupt occurs
The ongoing instruction flow needs to be altered to handle the event
Exceptions, interrupts and traps

## Slide 4: Exceptions, interrupts and traps
Exception: An unscheduled event that arises inside the CPU
  Overflow, illegal instruction, or divide by zero
  Synchronous (ie happen at times aligned to the flow of current instruction in the pipeline)
Interrupt: Events that are external to the processor, typically hardware driven
  Asynchronous, ie they can happen any time, not related to the instruction flow
Trap: An ‘interrupt’ generated by software
  Asynchronous
The terminology is hazy!!!

## Slide 5: What should you do when any of these happen?
Not: crash, ignore or do wrong things
Run some code that can address the contingency
How would you do that?
  Save current PC (to return to normal execution if required)
  Record the cause of the contingency
  Flush incomplete pipeline instructions (basically doing a jump…)
  Jump to the contingency handler
  Resume after handling contingency
How to store the PC?
  New register: EPC (Exception PC)
How to record the cause?
  New register: m_cause
How to jump to the new code?
  New register: mtvec (details to follow)
‘Control and Status Registers (CSRs)’
The ‘m’ is for ‘machine mode’

## Slide 6: Jumping to the handler
The mtvec register has two fields:
  Base [31:2]: 30 MSBs of the handler address
  Mode [1:0]: Determines how table behaves
Mode | Name | Description
00 | Direct | All traps (exceptions and interrupts) jump to BASE
01 | Vectored | Exceptions go to BASE, but Interrupts jump to BASE + (4 x cause)
Offset from BASE | Cause Code | Event Type | Description
+ 0 | 0 | Exception | All synchronous exceptions (Illegal Instr, etc.)
+ 4 | 1 | Interrupt | Supervisor Software Interrupt
+ 12 | 3 | Interrupt | Machine Software Interrupt
+ 20 | 5 | Interrupt | Supervisor Timer Interrupt
+ 28 | 7 | Interrupt | Machine Timer Interrupt
+ 36 | 9 | Interrupt | Supervisor External Interrupt
+ 44 | 11 | Interrupt | Machine External Interrupt

## Slide 7: Where can exceptions occur?
Stage | Example
IF | instruction fetch fault
ID | illegal instruction
EX | arithmetic overflow
MEM | page fault
WB | (rare)
Other sources:
System calls (intentional traps) Used for giving control to OS, asking OS to perform certain operation etc.
Examples
  Exit program, file read / write / open / close, get_time etc.

## Slide 8: Precise vs imprecise exceptions
Precise:
  All earlier instructions complete execution
  Faulty instruction identified
  All later instructions flushed
  System is in well-defined state
Imprecise:
  Some earlier instructions may not have completed
  Some later instructions may complete instead of flushing
  System state is inconsistent and undefined
  Often a result of out-of-order execution architectures
  Architectures that use separate units, such as FPUs, that complete at a different time than rest of the instruction