## Slide 1: Computer Architecture
Prof. Saurabh Gandhi (EEE department)

## Slide 2: Microprogramming
Pain points for hardwired FSM control
State explosion for rich ISAs
Difficult to modify / extend instruction set in a modular fashion
Difficult verification (verify everything after any modification
Irregular structure – difficult to optimize in silicon

## Slide 3: A computer inside the computer – making control itself a program
Break up instruction processing into microinstructions
Several microinstructions  single instruction
FSM State  microinstruction
Control signals for each microinstruction stored in ROM
µPC (Micro-Program Counter): Points to the current micro-instruction
Address Select Logic: Decides the next µPC (state transition in our FSM)

## Slide 4: Microprogramming – datapath

## Slide 5: Microprogramming – control
State | Pseudocode | IRLd | RegSel | RegWr | RegEn | ALd | BLd | ALUop | ALUen | MALd | MemWr | MemEn | ImmSel | ImmEn | mBr | Nxt
F0 | PC->MA, A | * | PC | 0 | 1 | 1 | * | * | 0 | 1 | 0 | 0 | * | 0 | N | 
F1 | Mem->IR | 1 | * | 0 | 0 | 0 | * | * | 0 | 0 | 0 | 1 | * | 0 | S | 
F2 | ALU->PC | 0 | PC | 1 | 0 | 0 | * | INC_A_4 | 1 | * | 0 | 0 | * | 0 | D | 
ADD0 | R[t1]->A |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADD1 | R[t2]->B |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADD2 | ALU->R[t0] |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ADD3 | GOTO F0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | F0
Controller is a state machine (FSM), with transitions defined as:
N: go to next state
S: do nothing (if ‘busy?’ is asserted) else next state
D: check opcode and func and go to correct state
J: Jump to a particular state
EZ, NZ: Jump if condition true else next state
Example: add t0 t1 t2

## Slide 6: Microsequencer

## Slide 7: Horizontal vs vertical microcode
Horizontal microcode:
One bit per signal (one-hot encoding in control word)
Wide control word
No decoding required
Example: 16 different alu operations will have 16 bits in the control word
Vertical microcode:
Signals are grouped into fields
Requires decoder between ROM and datapath
Example: 16 different alu ops encoded in 4-bits in control word

## Slide 8: Is microcoding relevant today?
CISC legacy: modern Intel/AMD processors are CISC outside, RISC inside
  Provide complex instructions in ISA, which are actually decoded into simpler RISC-like microoperation sequences
Patching hardware bugs: updates distributed via BIOS/OS upgrades to modify ROM (also called WCS – writable control store) to fix bugs
  Spectre / meltdown mitigations from Intel
Managing complex system-level algorithms
  Boot sequences, frequency scaling and power management
Hybrid designs: Fast frequent path (hardwired and pipelined) + slow rare path (complex and microcoded)

## Slide 9: Making things faster
Faster clocks
  Device speeds
  Datapath capacitance
  Clock skew
  Power consumption and thermal limit
Faster devices
  Physical limits (electrons have finite velocity)
  Memory is inherently very slow!
Parallelize instructions

## Slide 10: Pipelined multi-cycle processors
Does not change the latency of individual instructions
Increases the throughput of instructions
Speedup ∝ #stages
Rate limited by slowest stage

## Slide 11: Pipelined RISC-V processor

## Slide 12: What about control?
How do we modify the control circuit from the single cycle control?
Pipeline control bits!

## Slide 13: Pipelined datapath and control
What problems do you see here?

## Slide 14: Pipelining hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy
  (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data write
Control hazard
  Flow of execution depends on previous instruction

## Slide 15: Structural hazard
Problem: Two or more instructions in the pipeline compete for access to a single physical resource
Solution 1: Instructions take turns using resource, some instructions have to stall (wait)
Solution 2: Add more hardware to machine
Can always solve a structural hazard by adding more hardware
Multiple ports to the regfile solves the access problem
Is this a problem for Harvard or von Neuman architecture (or both)?
Soln: Separate data and instruction caches
ISA designed to avoid multiple accesses

## Slide 16: Data hazards
RAW: Read After Write (instruction tries to read before previous instruction has finished writing)
WAR: Write After Read (instruction writes to a register before a previous instruction has read from it)
WAW: Write After Write (instruction writes to a register before an earlier instruction writes to it)

## Slide 17: Data hazard solution – bubbles (stalling)
Bubbles: affected pipeline stages do “nothing” for a cycle.
How many bubbles in RAW?
Stalls reduce performance
How to mitigate stall performance degradation?
Compilers can arrange the instructions such that these conditions are avoided
  Compilers must know how the pipeline is implemented and how instructions interact
Reduced one stall

## Slide 18: Data hazard solution – forwarding
Forwarding:
Data already available in cycle 3
Grab it from pipeline stage, rather than waiting to update the register file
Needs changes in datapath hardware as well as extra control signals!

## Slide 19: Data hazard solution – forwarding

## Slide 20: Data hazards – forwarding does not always work!
Hardware can stall the pipeline – hardware interlocks
Slot after ‘load’ is called a ‘load delay slot’
Re-ordering code, if possible, is always a good solution!
Analyze this RAW hazard. What will you forward?