## Slide 1: Computer Architecture
Prof. Saurabh Gandhi (EEE department)

## Slide 2: Memory Technology: 1950s
1948: Maurice Wilkes examining
EDSAC’s delay line memory tubes
16-tubes each storing 32 17-bit words
Maurice Wilkes: 2005
1952: IBM 2361 16KB magnetic core memory

## Slide 3: Memory Technology Today: DRAM
DDR SDRAM
  Double Data Rate
  – Synchronous Dynamic RAM
  The dominant memory technology in PC market
  Delivers memory on the positive and negative edge of a clock (double rate)
  Generations:
    DDR (MemClkFreq x 2(double rate) x 8 words)
    DDR2 (MemClkFreq x 2(multiplier) x 2 x 8 words)
    DDR3 (MemClkFreq x 4(multiplier) x 2 x 8 words)
    DDR4 (released in 2014)
    DDR5 (in Q3 2021)

## Slide 4: DRAM Capacity Growth
Unprecedented growth in density, but we still have a problem

## Slide 5: Processor-DRAM Performance Gap
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
DRAM
CPU
1982
Performance
Time
“Moore’s Law”
Memory Wall:
1GHz Processor  1 ns per clock cycle
50ns for DRAM access  50 processor clock cycles per memory access!

## Slide 6: Faster Memory Technology: SRAM
SRAM
6 transistors per memory cell
 Low density
Fast access latency of 0.5 – 5 ns
More costly
Uses flip-flops
DRAM
1 transistor per memory cell
 High density
Slow access latency of 50-70ns
Less costly
Used in main memory
A SRAM Cell

## Slide 7: Slow Memory Technology: Magnetic Disk
Typical high-end hard disk:
Average Latency: 4 - 10 ms
Capacity: 500-2000GB

## Slide 8: Quality vs Quantity
 | Capacity | Latency | Cost/GB
Register | 100s Bytes | 20 ps | $$$$
SRAM | 100s KB | 0.5-5 ns | $$$
DRAM | 100s MB | 50-70 ns | $
Hard Disk | 100s GB | 5-20 ms | Cents
Ideal | 1 GB | 1 ns | Cheap
Memory
(DRAM)
Devices
Input
Output
Processor
Control
Datapath
Registers
(Harddisk)

## Slide 9: Just how slow is the school bus?
Caches use static RAM (SRAM)
Fast (typical access times of 0.5 to 2.5 ns)
Higher power, expensive ($2000 to $4000 per GB in 2011)
Static: content will last as long as power is on
Main memory uses dynamic RAM (DRAM)
Lower power, cheaper ($20 to $40 per GB in 2011)
Slower (typical access times of 50 to 70 ns)
Dynamic: needs to be “refreshed” regularly (~ every 8 ms)

## Slide 10: Tradeoffs across a variety of memory technologies

## Slide 11: Best of Both Worlds
What we want:
  A BIG and FAST memory
  Memory system should perform like 1GB of SRAM (1ns access time) but cost like 1GB of slow memory
Key concept:
Use a hierarchy of memory technologies:
  Small but fast memory near CPU
  Large but slow memory farther away from CPU

## Slide 12: Writing reports before the age of internet – an analogy
You have to write a report on the ‘History of computers’, by referring books in the library
You pick 2-3 relevant books and sit at a desk to read
You realize you need to refer to a few more books; what do you do?
Keep the current books on the desk and bring the new ones you need
All the books that you may need are on the desk, easily accessible
Only a small fraction of the total number of books in the library
You are done and want to write the next report on semiconductor technology – what do you do?
Return all ‘history of computer’ books to the shelves and bring ‘semiconductor’ books to your desk

## Slide 13: The stack of books on your desk is called a cache

## Slide 14: The principle of locality
Programs access only a small portion of memory address space at a given time
Instructions
Sequential execution
Loops
Data
Arrays
Structs
Stack
Heap
Temporal Locality (locality in time)
Go back to the same book on desk multiple times
If a memory location is referenced, then it will tend to be referenced again soon
Spatial Locality (locality in space)
When go to shelves, grab many books on computers since related books are stored together
If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
Caches: Use the principle of locality to create the illusion of memory being almost as fast as fastest memory and almost as large as biggest memory of the hierarchy

## Slide 15: Working Set: Definition
Set of locations accessed during t
Different phases of execution may use different working sets
Our aim is to capture the working set and keep it in the memory closest to CPU

## Slide 16: Two Aspects of Memory Access
How to make SLOW main memory appear faster?
  Cache – a small but fast SRAM near CPU
  Hardware managed: Transparent to programmer
How to make SMALL main memory appear bigger than it is?
  Virtual memory
  OS managed: Transparent to programmer
Memory
(DRAM)
Devices
Input
Output
Processor
Control
Datapath
Registers
Cache
(SRAM)
(Harddisk)

## Slide 17: What is a cache?
Memory Cache
  Holds a copy of a subset of main memory
  We often use $ (“cash”) to abbreviate cache (e.g. D$ = Data Cache, L1$ = Level 1 Cache)
Modern processors have separate caches for instructions and data, as well as several levels of caches implemented in different sizes
Implemented with same IC processing technology as CPU and integrated on-chip
  Faster but more expensive than main memory

## Slide 18: Memory hierarchy
L3: Engineering section
L2: All books on Computers
L1: History of computers
How do we manage all the books in different locations?
When to go to L1 / L2 / L3 / Main memory?
When to bring a book from shelf to cupboard?
When to bring from cupboard to desk?
If desk is full, which book to put back?

## Slide 19: Memory transfer in the hierarchy
registers ↔ memory By compiler (or assembly level programmer)
cache ↔ main memory By the cache controller hardware
main memory ↔ disks (secondary storage)
  By the OS (virtual memory)
  Virtual to physical address mapping assisted by the hardware (TLB)
  By the programmer (files)

## Slide 20: Cache management – four important questions to resolve
Where to put the data? When we copy a block of data from main memory to the cache, where exactly should we put it?
How to find the data? How can we tell if a word is already in the cache, or if it has to be fetched from main memory first?
How to replace data? Eventually, the small cache memory might fill up. To load a new block from main RAM, we’d have to replace one of the existing blocks in the cache... which one?
How to write data? How can write operations be handled by the memory system?

## Slide 21: Question 1: Where to put the data?
Direct-mapped cache:
Each main memory address maps to exactly one cache block
For example, on the right is a 16-byte main memory and a 4-byte cache (four 1-byte blocks)
Memory locations 0, 4, 8 and 12 all map to cache block 0
Addresses 1, 5, 9 and 13 map to cache block 1, etc.
How can we compute this mapping?
main memory
cache

## Slide 22: Question 1: Where to put the data?
Computing the mapping – modulo operation
If the cache contains 2k blocks, then the data at memory address i would go to cache block index i mod 2k
For instance, with the four-block cache here, address 14 would map to cache block 2
14 mod 4 = 2
main memory
cache

## Slide 23: Question 1: Where to put the data?
Computing the mapping – least significant address bits
main memory
cache
Look at the least significant k bits of the address
With our four-byte cache we would inspect the two least significant bits of our memory addresses
Address 14 (1110 in binary) maps to cache block 2 (10 in binary)
Taking the least k bits of a binary value is the same as computing that value mod 2k

## Slide 24: Question 2: How to find the data?
Given a main memory address, we know where to put it in the cache
When the CPU wants to read data at a particular main memory address, how can it check whether the cache contains the data?
Problem: Different main memory locations map on to the same location in the cache
For instance, cache block 2 could contain data from addresses 2, 6, 10 or 14
Solution: Store ‘tags’ along with the data to identify the source
main memory
cache

## Slide 25: Question 2: How to find the data?
What are tags?
<Tag><index> == main memory address!

## Slide 26: Question 2: How to find the data?
The valid bit
The cache starts out empty, so how do we know if at any location, it is actual data or the default value?
Add a ‘valid’ bit to each location: 0 means invalid and 1 means data is valid

## Slide 27: Taking advantage of spatial locality
Solution: make the cache block size larger than one byte
If we access 0, we are likely to access 4 and perhaps 8 also… but we are keeping only one of them in the cache

## Slide 28: Locating a byte within the cache block – block offsets
Assume we have a cache with 2k blocks, each containing 2n bytes
k bits of the address will select one of the 2k cache blocks
The lowest n bits are a block offset within the block

## Slide 29: A circuit to implement direct-addressed cache

## Slide 30: A circuit to implement direct-addressed cache

## Slide 31: Disadvantage of direct mapped cache
Rendered ineffective!
Cache may also be wasted – empty slots
What about replacement policy? Do we need one?

## Slide 32: Fully associative caches
Store data in any (unused) cache block (where to put the data)
What is the trade-off here?
How to find data?
Entire address must be used as tag (more cache ‘wasted’)
Data can be in any cache block, so each tag must be compared to the address to check if data is available in the cache!
How many comparators do you need?
= # cache blocks
How parallel?
Content Associative Memory – expensive and power hungry

## Slide 33: Set associative caches
Somewhere in between direct mapped and fully associative caches
Cache divided into groups of blocks called sets
Each memory address maps to exactly one set, but it can be in any block within the set
If each set has 2x blocks, it is said to be 2x-way associative cache
Example: we have a cache with 8 blocks:

## Slide 34: Question 1: Where to put the data (set associative caches)
What set does the data belong to? Within the set it can be put anywhere
Assume the cache has 2s sets, and each block has 2n bytes
This means all memory address blocks must map to one of the 2s sets
ie least s bits of address determine the set address (set index)
But…
Least n bits of address determine the block offset within the block
So the next s bits give the set and the remaining bits will be tag

## Slide 35: Question 2: How to find the data?
We want to find data with memory address 6195 (just an example); cache has 8 blocks with 16 bytes per block
6195 in binary is 00...0110000 011 0011
How many bits is the block offset?
4
How many sets do we have for 1-way, 2-way and 4-way designs?
8, 4 and 2
How many bits do we need for set index?
3, 2 and 1
Set index for our address will be:
011 for 1-way; 11 for 2-way; and 1 for 4-way
Data can go in any block within the set
Found by searching for tag!

## Slide 36: Implementation of a set-associative cache

## Slide 37: Set associative caches are a general idea
1- way set associative == direct mapped
If a cache has 2k blocks, a 2k-way set associative cache would be the same as a fully-associative cache.

## Slide 38: Review of different types of caches

## Slide 39: Question 3: How to remove data to make space for new data?
Block replacement policies
Need to replace a block only if no more empty blocks left in the set and we need to load data
Best policy: remove what will not be needed for the longest time (cannot know beforehand)
Random replacement
Queue based: FIFO, LIFO, FILO
Recency-based: Least Recently Used (LRU), Most Recently Used (MRU), Time-aware LRU
Frequency-based: LFU, MFU (?)
https://en.wikipedia.org/wiki/Cache_replacement_policies for an extensive list
LRU
Have to keep track of ‘last used’ for each block

## Slide 40: Example of LRU
Assume a fully-associative cache with two blocks, which of the following memory references miss in the cache?
Also assume distinct addresses go to distinct blocks

## Slide 41: How to write data?
Write-through policy
Always write data to cache and the memory (i.e. never write to cache-only)
  Cache and memory are always forced to be consistent – good!
  Each memory write access as slow as main memory access – slow!
  Write to a ‘buffer’ and separate hardware updates main memory while processor moves forward
Write-back policy
Write data only to cache; update memory when the block is removed
  Cache and memory can be inconsistent for some time
  Multiple writes to the same block collected in the cache; written back together
  Dirty bit: Extra bit for each cache block to indicate whether it needs to be written back
Write-allocate policy
If there is a miss for a write, bring that data into cache and then update it
  Typically paired with write-back
No write allocate: just change the main memory directly
  Typically paired with write-through

## Slide 42: A picture of the cache

## Slide 43: Fully associative cache example operation

## Slide 44: Fully associative cache example operation

## Slide 45: Fully associative cache example operation

## Slide 46: Direct mapped cache example operation

## Slide 47: Set-associative cache example operation

## Slide 48: Cache terminology
Cache hit: Cache contains valid copy of the block, so return the data
Cache miss: Cache does not contain the desired data, so copy it over from main memory into an empty slot
  Replace a slot if all slots are full
How effective is the cache?
Hit rate (HR): percentage of memory accesses (of a program) that result in hit
Miss rate (MR): percentage that result in miss
MR = 1 – HR
How fast is the cache?
Hit time (HT): Time to access cache (including all operations like matching the tag)
Miss penalty (MP): Time to replace a cache block from a lower level

## Slide 49: Access time for memory with caches
In a machine without caches, what is the memory access time?
Fixed number of cycles (say 1000)
How does access time change with the introduction of caches?
If hit – hit time
If miss – miss penalty
Variable access time
We can talk about an average access time

## Slide 50: Average Memory Access Time (AMAT)
Consider a 2-level hierarchy which has a cache and main memory:
AMAT = (Hit rate * Time to go to cache) + (Miss rate * Time to go to memory)
= (Hit rate * Hit time) + (Miss rate * (Miss penalty + Hit time))
= (Hit rate * Hit time) + (Miss rate * Hit time) + (Miss rate * Hit penalty)
= Hit time + Miss rate × Miss penalty
AMAT = Hit time + Miss rate × Miss penalty
How do the different cache parameters affect AMAT?

## Slide 51: Optimizing AMAT = Hit time + Miss rate × Miss penalty
Hit time
How many comparisons you need to do
Cache size
  Smaller is better
Associativity
  Lower is better
Miss rate
Access pattern of your program
  Example: apply f(x) to all values in an array
  Apply to blocks of array at a time: good
  Apply to elements picked at random / out-of-order: bad
Block size
  Bigger is better
Cache size
  Bigger is better
Associativity
  Higher is better (keeps the data in cache longer)
Miss penalty
Hierarchy depth
  Lower is better
Block size
  Lower is better

## Slide 52: Sources of cache misses
Compulsory: (Many names: cold start, process migration (switching processes), 1st reference)
First access to block impossible to avoid; Effect is small for long running programs
Increase block size
But this increases MP; very large blocks could increase MR
Capacity:
Cache cannot contain all blocks accessed by the program, so full associativity won’t hold all blocks
Increase cache size
But may increase HT
Conflict: (collision)
Multiple memory locations mapped to the same cache location, so there is a lack of associativity
Increase associativity
But may increase HT

## Slide 53: Identifying the three types of misses

## Slide 54: AMAT Example
Processor specs: 200 ps clock, miss penalty of 50 clock cycles, miss rate of 0.02 misses/instruction, and hit time of 1 clock cycle.
Which of the following improvements will decrease (better) our AMAT the most?
AMAT = 1 + 0.02 * 50 = 2 cycles = 400 ps
190 ps clock
  2 cycles = 380 ps
Change miss penalty to 40 cycles
  1 + 0.02 * 40 = 360
Change miss rate to 0.015 per instruction
  1 + .015 * 50 = 350

## Slide 55: Summarizing parameter trade-offs in cache design
To make AMAT small, we want to have a small hit time, low miss rate, and/or small miss penalty
It is hard to do all these at once!
  Direct mapped caches have small hit time
  Fully-Associative caches have a low miss rate
  Small blocks help with lowering miss penalty, so do many opportunities to store data
Can we combine all these things into one structure to achieve our goal?
Multi-level caches!

## Slide 56: Multi-level cache design
L1$ focus on low hit time
  Small size (less comparisons)
  Low associativity (less comparisons)
  OK to have a higher miss rate because there is L2$...
L2$, L3$ focus on low miss rate
  Larger cache
  Larger blocks
  Larger associativity

## Slide 57: Multi-level cache AMAT
AMAT = L1 HT + L1 MR × L1 MP
Now L1 MP depends on other cache levels
Must trace ENTIRE path to memory
L1 MP = L2 HT + L2 MR × L2 MP
If more levels, then continue this chain (i.e. MPi = HTi+1 + MRi+1 × MPi+1)
Final MP is main memory access time
For two levels: AMAT = L1 HT + L1 MR × (L2 HT + L2 MR × L2 MP)

## Slide 58: AMAT Example 2
Processor specs:
1 cycle L1 HT, 2% L1 MR,
5 cycle L2 HT, 5% L2 MR,
100 cycle main memory HT
Calculate AMAT:
without $L2, with $L2
3 1.3
2 1.2
2 1.1
3 1.2
AMAT1 = 1 + 0.02 × 100 = 3
AMAT2 = 1 + 0.02 × (5 + 0.05 × 100) = 1.2

## Slide 59: Effect of block and cache sizes, associativity on Miss Rate

## Slide 60: Example cache configurations
Why software developers should care about caches: https://medium.com/software-design/why-software-developers-should-care-about-cpu-caches-8da04355bb8a

## Slide 61: Questions on cache

## Slide 70
C: cache size; K: block size; N: set size